## Slide 1
KINETROL

## Slide 2
The Kinetrol Advantage
• Privately owned for over 50 years
• All parts (actuators and accessories) are engineered and made in-house to guarantee quality.
• Manufactured in three sites in Farnham, England.
+44 (0) 1252 733838
kinetrol.com

## Slide 3
+44 (0) 1252 733838
kinetrol.com
Kinetrol is not a “lunch box” actuator
Problem solver
Niche applications
Different shape
What makes Kinetrol different?
Think Outside the Box

## Slide 4
+44 (0) 1252 733838
kinetrol.com
One Piece Shaft and Vane
Constant Output Torque
Compact and Efficient
Double Opposed Polyurethane Lip Seals
Single Moving Part
Unique Features
Zero hysteresis for V-ball control applications
Kinetrol matches the torque output of metal seated ball valves throughout the entire stroke
Best torque/size package available, fastest operating speeds and lowest air consumption
Pressure assisted for long life (no “O” rings)
Most reliable mechanism for 1/4 turn actuation

## Slide 5
+44 (0) 1252 733838
kinetrol.com
High Cycle
Quick Opening/Closing
High Temperature
Metal Seated Ball Valves
Most Suited Applications
Control Applications (V-Ball Valves)
Space Constraints

## Slide 6
+44 (0) 1252 733838
kinetrol.com
High Cycle Applications
Kinetrol actuators are guaranteed to 4,000,000 cycles because they last
Typical Applications are:
• Bottle filling
• Injection mold cooling
• Batch processes

## Slide 7
+44 (0) 1252 733838
kinetrol.com
Internally, Kinetrol actuators have almost no "Dead space”
Internally, Rack & Pinion actuators have lots of “Dead space”
“Dead space"
“Dead space"
The majority of the plant air supply is being used to move the vane, rather than fill in dead space.
That’s why Kinetrol’s have such fast open/close times
Fast Open/Close Times

## Slide 8
+44 (0) 1252 733838
kinetrol.com
“Dead space"
Compare “Dead Space” to see why Kinetrol actuators operate faster
KINETROL
COMPETITION
Smaller “Dead space” = faster open/close times
“Dead space"

## Slide 9
+44 (0) 1252 733838
kinetrol.com
Comparing a Kinetrol to a typical Rack & Pinion actuator ”Dead Space” = ”Cost”
“Dead space”
(In Red)
Cost of Operation
How do we quantify this volumetric efficiency?
Rack & Pinion – Considerably greater dead volume: More air per stroke = less efficiency
Kinetrol – The vane design has built up sideplates to keep dead volume to a minimum

## Slide 10
Kinetrol - Model 07
- 95 Nm @ 5.5 bar
Flowserve Norbro - Model 20-40R
- 109 Nm @ 5.5 bar
Air Torque - Model AT251D
- 101 Nm @ 5.5 bar
El-O-Matic - Model FD100
- 105 Nm @ 5.5 bar
Cost of Operation
(Double Acting Actuator Comparison)
+44 (0) 1252 733838
kinetrol.com

## Slide 11
Flowserve - Total volume per cycle: (0.69 + 0.74) = 1.43 litres
Air Torque - Total volume for one complete cycle: (0.51 + 0.78) = 1.29 litres
El-O-Matic -Total volume per cycle: (0.6 + 0.3) + (0.9 + 0.3) = 2.1 litres
Cost of Operation
(Air/Energy Consumption Comparison)
+44 (0) 1252 733838
kinetrol.com
Kinetrol - Total volume per cycle: (0.342 x 2) = 0.684 litres

## Slide 12
Cost of Operation
(Air/Energy Consumption Comparison)
+44 (0) 1252 733838
kinetrol.com
Air Torque - (1.29L/0.684L) x (95Nm/101Nm) = 1.77
Flowserve Norbro - ( 1.43L/0.684L) x (95Nm/109Nm) = 1.82
El-O-Matic - (2.1L/0.684L) x (95Nm/105Nm) = 2.77
The torque specific (L/Nm) energy consumption of these actuators are 1.77, 1.82 or 2.77 times that of the equivalent Kinetrol actuator

## Slide 13
High Temperature Applications
• Beside Boilers
• Beside Furnaces
• Installed on high temperature valves
+44 (0) 1252 733838
kinetrol.com
Examples of high ambient applications are:
Kinetrol can be installed with Viton seals for high ambient temperatures.

## Slide 14
+44 (0) 1252 733838
kinetrol.com
Kinetrol Actuator torque matches the valve perfectly
Sizing Actuators – Kinetrol
Typical Kinetrol Torque

## Slide 15
+44 (0) 1252 733838
kinetrol.com
Sizing Actuators - Rack & Pinion
Typical Torque for a Rack & Pinion Actuator
End of stroke torque of Rack & Pinion isn’t enough to close the valve

## Slide 16
+44 (0) 1252 733838
kinetrol.com
Run torque of Scotch Yoke actuator isn’t enough to close the valve
Danger zone: Valve shaft will break
Sizing Actuators – Scotch Yoke
Larger Symmetrical Yoke Actuator Torque Curve
Typical Symmetrical Yoke Actuator Torque Curve
MAST (Maximum Allowable Shaft Torque)
Solution: Use a larger actuator
Problem: Actuator torque is too much for the valve shaft

## Slide 17
• Valve manufacturers design the shafts to be as efficient as possible
• All shafts have a “MAST” (Maximum allowable shaft torque)
• When the actuator torque exceeds the MAST, the shaft will break
+44 (0) 1252 733838
kinetrol.com
Sizing Actuators

## Slide 18
Rack & Pinion, and Scotch Yoke Actuators
Rotary Control Applications (V-Ball Valves)
+44 (0) 1252 733838
kinetrol.com
aaaaaa
To Rotary
Both quickly start to get hysteresis, which means you don’t control your process well
With Kinetrol’s direct mount positioner and anti-backlash coupling, any movement from the positioner results in an identical movement in the valve
Precise, Pin Point Accuracy
Scotch Yoke’s wear out and become “sloppy”
Kinetrol
Rack and pinion’s wear out and become “sloppy”
Change Linear Motion
Uses rotary motion to operate rotary valves

## Slide 19
Space Constraints
+44 (0) 1252 733838
kinetrol.com
Kinetrol Actuators
(Tall and skinny)
Kinetrol’s are a different shape than other actuators
Scotch Yoke/Rack & Pinion
(Short and Fat)
They often fit in places where scotch yoke, and rack & pinion actuators can’t
Think Outside the Box
Notes: Position 1 - Horizontal pipeline, vertical stem:
In this orientation, a bracket is acceptable
Position 2 - 45 degree pipeline, vertical stem:
In this orientation, a bracket is not acceptable. The bracket will bend and create side-loading on the actuator because it is weak. A bracket is not recommended because you want to be able to use the valve/actuator in any orientation.
Position 3 - Vertical pipeline, horizontal stem:
In this orientation, a bracket is not acceptable. The bracket will bend and create side-loading on the actuator because it is weak. A bracket is not recommended because you want to be able to use the valve/actuator in any orientation.
Position 4 - Horizontal pipeline, horizontal stem:
In this orientation, a bracket is not acceptable. The bracket will bend and create side-loading on the actuator because it is weak. A bracket is not recommended because you want to be able to use the valve/actuator in any orientation.

## Slide 20
+44 (0) 1252 733838
kinetrol.com
Scotch yoke actuators are not symmetrical
Side-loading causes packing leaks which lead to premature failure of the valve
Side-loading

## Slide 21
The Kinetrol Advantage
Kinetrol’s aren’t a typical “lunch box” type actuator, SO
+44 (0) 1252 733838
kinetrol.com
And use them in applications where rack & pinion or scotch yoke actuators don’t perform
Think Outside the Box